## Slide 1: DIGITAL ALARM CLOCK USING NEXYS-4 ARTIX -7 FPGA BOARD
Name: Movva Maheswara Naga Vardhan Sarma
Reg No:12009874
Roll No: RKMO48A05
Presented To: Jyotirmoy Pathak
SCHOOL OF COMPUTER SCIENCE AND ENGINEERING
LOVELY PROFESSIONAL UNIVERSITY

## Slide 2: AGENDA
Introduction to Nexys-4 Artix-7 FPGA Board
Block Diagram of Digital Alarm Clock
Master XDC Blocks
Modules
RTL
Simulation
Working on Digital Alarm Clock on FPGA
Power and Time Analysis

## Slide 3: Introduction to Nexys-4 Artix-7 FPGA Board

## Slide 4: Features
Xilinx Artix-7 FPGA XC7A100TCSG324-1
15,850 logic slices, each with four 6-input LUTs and 8 flip-flops
4,860 Kbits of fast block RAM
Six clock management tiles, each with phase-locked loop (PLL)
240 DSP slices
Internal clock speeds exceeding 450 MHz
On-chip analog-to-digital converter (XADC)
A 128 Mbit cellular RAM (pseudo-static DRAM)
• A 128 Mbit non-volatile serial flash device

## Slide 5: Connectivity and Onboard I/O
SD: microSD card connector
Pmod Connectors: 4 Pmod ports
VGA:12-bit VGA port
Audio: PWM audio output
Temp sensor: One temperature sensor
Display: 2*4-digit seven segment displays
Switches: 16
Buttons: 4
LEDs:16
Tri-color LEDs: 2

## Slide 6: Description about the Switches and Pushbuttons

## Slide 7
TimeSettingMode: If the [sw15] is high then it allows the increment operation of the Minute and Hour in the FPGA using the [Increment Minute] BTNL and [IncrementHour] BTNR using pushbuttons. If the [sw15] is low, then it is automatically under the control of the clock.
TimeReset: If the [sw14] is high then it Reset the time else does not Reset.
AlarmReset: If the [sw13] is high then it Reset the Alarm else does not Reset.
EnableAlarm: If the [sw12] is high then the comparison of time and alarm is equal to the [LED0] high.
DisplayAlarm: If the [sw11] is high then it displays the Alarm in Seven Segment Display

## Slide 8
IncMin: If [BTNL] pushbutton is high and TimeSettingMode is high then it changes the Time Minute
IncHour: If [BTNR] pushbutton is high and TimeSettingMode is high then it changes the Time Hour
IncAlarmMin: If [BTNU] pushbutton is high and Display Alarm is high then it changes the Alarm Minute
IncAlarmHour: If [BTND] pushbutton is high and Display Alarm is high then it changes the Alarm Hour.

## Slide 9: For Time

## Slide 10: For Alarm

## Slide 11: BLOCK DIAGRAM

## Slide 13: Working on Digital Alarm Clock on FPGA

## Slide 14: Master XDC Blocks

## Slide 17: Modules
Time Module
Alarm Module
Comparator Module
7-Segment Display Driver Module
Debouncing Pushbutton Module

## Slide 18: CLOCK DIVIDER CALCULATION FOR 1Hz

## Slide 19: Time Module

## Slide 21: Alarm Module

## Slide 23: Comparator Module

## Slide 25: 7-Segment Display Module

## Slide 26: CLOCK DIVIDER FOR 10KHz

## Slide 27
FSM SEVEN SEGMENT DISPLAY DRIVER FOR TIME MODULE

## Slide 28
FSM SEVEN SEGMENT DISPLAY DRIVER FOR ALARM MODULE

## Slide 30: Pushbutton Debouncing

## Slide 31: Internal Structure

## Slide 32: Detail Waveform

## Slide 34: RTL

## Slide 35: Internal View

## Slide 36: Simulation

## Slide 37: Power and Time Analysis

## Slide 38: POWER ANALYSIS

## Slide 39: TIME ANALYSIS

## Slide 40: Thank You